Arduino Automatic Light Using LED
In the circuit, the values from the photoresistor are obtained and used to control the LED’s brightness. The photoresistor’s resistance changes with light intensity, which in turn changes the voltage across it. This voltage is read by the Arduino, which then adjusts the current flowing to the LED, thereby controlling the LED’s light intensity.

https://arduinopoint.com/ldr-arduino-project/
Arduino Automatic Light Using Relay Schematics
The relay is a switch controlled by an electrical signal. In this project, it’s used to control a bulb. Like the LED, but the voltage is being sent to a 5V Relay Module, that acts like a bottleneck and tells the module how much current to send to the lght bulb.
It is connected to NO, normally open pin, which means the common pin is connected only if the relay is triggered, and in this case, it’s triggered by the voltage received from the board.
This circuit might be dangerous, touching the circuit might be the same as sticking one’s finger inside a power outlet’s socket.

https://arduinopoint.com/ldr-arduino-project/

Arduino Automatic Light Tracker
The circuit is the same as in the LED, expect there should be at least two photoresistors to get the information on the brightest spot around the light tracking object. The Arduino reads the voltage from the photoresistors and uses this information to control a micro-servo motor. The motor rotates a light tracker towards the brightest point. This allows the light tracker to continuously follow the brightest light source in real-time.